## Slide 1
A New Look at the Gortdrum Copper Deposit, Co. Tipperary (+ bonus Limerick content!)
Eoin Dunlevy1,2, Koen Torremans1, Mark Holdstock3, and Murray Hitzman1
1iCRAG / UCD, 2Terranta GmbH, 3Group Eleven Resources

## Slide 2
Historic mining district (Zn, Pb, Cu, Ag)
  Oola + Gortdrum
  Over 50 Mt @ Pallas Green + Stonepark
  Several small prospects
Zn/Pb mineralisation hosted in Waulsortian
Cu mineralisation hosted in LLS/Ballysteen
Kerr, 2013
Silvermines
17.7 Mt @ 8.96 %
Zn +Pb
Gortdrom 3.81 Mt
@ 1.19% Cu
1Kilbricken
2.7 Mt @ 8.8 %
Zn + Pb *
2Stonepark
5.1 Mt @ 11.3 %
Zn + Pb
3Pallas Green
45.4 Mt @ 8 %
Zn + Pb
1 Colthurst & Reed (2019) Kilbricken NI 43-101.
2Gordon et al. (2018), Stonepark NI 43-101
3Glencore Resources & Reserves report 2018
Courtbrown
Rathkeale
Kilmallock
Aherlow
(Cu/Ag)
Carrickittle
Geology modified from GSI 100K series
Lower Palaeozoic Basement
Devonian ORS
Lower Limestone Shales
Ballysteen Limestone
Waulsortian Mudmounds
Lough Gur
Knockroe Volc.
Herbertstown Fm.
Knockseefin Volc.
Dromkeen Fm
Namurian Clastics
Visean Shelf
Visean Basinal
Limerick Syncline
Historic Mine
Mineral Resource
Prospect
Region Overview
Ballywire
Knockfierna Inlier, looking north
ORS + Volcanic rocks
Lower Carboniferous Basin
Shannon Estuary
Notes: Metal endowed region
Challengin exploration under cover (ORS inliers vs open planes of lower Carboniferous)

## Slide 3
Rathkeale
Castleconnel Syncline
Limerick Syncline
Golden
Gulf
W
Gortdrum
Lithostratigraphy
Lithofacies variations mapped in 54 boreholes in Limerick Region
4 stratigraphic domains defined across the Limerick region
  Differentiation apparent from Waulsortian onward
Intra-formational lithology variations mapped in each formation
Rathkeale
Castleconnel
Syncline
Limerick Syncline
Golden
Gulf
E

## Slide 4
Blue Book
Summary Sections

## Slide 5
NE
SW
Formations thin onto Silvermines High
Expanded Waulsortian section in Rathkeale/Adare
Rathkeale to Silvermines
107 m
27 m
258 m
530 m
Flattened to Waulsortian
Notes: One important take away here is that earlier works by Somerville & Strogen suggested the Wauslortian was in excess of 1000 m moving westward.
This was before we had the drill control that we have now.
The estimation was based on extrapolation of a trend and not actual data. Available boreholes suggest a thickness up to 650m in the Kilmallock area (see slide 8)

## Slide 6
Blue Book
Summary Sections

## Slide 7
SE
NW
Growth into the Limerick Syncline
Limerick Syncline
Golden Gulf
Courtbrown
Rathkeale / Adare
Stonepark &
Pallas Green
Gortdrum
Oola
Ballywire
Rathkeale
/ Killeen
Courtbrown
Carrickittle
530 m
510 m
278 m
240 m
Courtbrown to
the Golden Gulf
Flattened to Waulsortian

## Slide 8
BB Summary Sections
Blue Book
Summary Sections

## Slide 9
BB Summary Sections
SE
500m growth in Waulsortian
ORS inliers –
No data
Kilmallock /
Bulgaden
Courtbrown
530 m
+650 m
135 m
NW
Courtbrown to
Galtee Mountains
Flattened to Waulsortian

## Slide 10
Main Outcomes
Several regional intraformational lithofacies variations established
Improved biostratigraphic constraints
Thickness distributions helping to define main depocentres and key structures
Irish Lower Carboniferous Lithostratigraphy - The Blue Book Project

## Slide 11
+ 500m Waulsortian growth
Reef dies out
into Golden Gulf
Reef grows into Syncline
accommodation
Reef thins onto high @ Ballywire (+ diatreme)
Notes: Ballywire, Aherlow and 3582/47 high possibly the same high?

## Slide 12
Discovered in 1963 by soils + IP
Operated 1967 - 1975
Copper – Silver Deposit
Ore Reserves of 3.81 Mt @ 1.19% Cu + 25.1 g/t Ag (Steed, 1986)
Hosted in Lower Limestone Shales & Ballymartin Limestone
Ore sits within ~ 100 m of the Gortdrum Fault
Spatial association with intrusions
  Analogies to Stonepark / Pallas Green
Gortdrum Open Pit
Gortdrum Mine
0.5 % Cu
1 % Cu
Steed (1975)
Notes: The open pit has a fish farm + the tailings pile is earmarked for a 43MW Solar PV developement

## Slide 13
Approximately 430 drillholes (mine + regional exploration)
Drillholes reinterpreted to conform with modern nomenclature
Structure and Stratigraphy evaluated and interpreted in 3D modelling packages
Gortdrum Mine
Notes: One of the issues with the Limerick region is the poor constraint on faulting (particularly around the Limerick Syncline @ Stonepark & Pallas Green)
The original aim of this study was to better constrain fault system behaviour in a data dense area, to apply lessons learned to data poor areas
Displacement on Gortdrum Fault dies out into the Emly Inlier.
Next structure of similar scale along strike is the Cullen Fault

## Slide 14
Orebody (0.5% Cu)
3D Model of Gortdrum Fault System
Reinterpretation of mine + exploration drilling
  Structure + Stratigraphy
Gortdrum Fault system is a segmented system
  Segments 750 – 1 km long with 100 m throw
  Previously mapped as through going structure
Mineralisation sits at the maximum fault throw
Elevation at Top ORS
Fault Segments
3D View
Gortdrum Mine
Next Slide
Notes: Orebody was digitised from open file cross sections (represents 0.5% Cu)

## Slide 15
Chart: Along fault
| 0 | 64 | 185 | 245 | 307 | 368 | 429 | 490 | 532 | 561 | 584
Gortdrum 1 | 15 | 28 | 51 | 69 | 84 | 94 | 102 | 100 | 93 | 93 | 92
Gortdrum 1-2 | 89 | 85 | 88 | 88 | 86 | 81 | 78 | 76 | 70 | 66 | 67 | 48
Gortdrum 3 | 58 | 87 | 98 | 67 | 65
Gortdrum 4 | 78 | 70 | 76 | 84 | 88 | 76 | 59 | 69 | 30 | 0
Base Mixed Beds / Top ORS
Gortdrum 4
Gortdrum 3
Gortdrum 1 & 2
Relay Ramp
Gortdrum Mine
Possible NW fault between
Gortdrum 2 & 3
Fault throws @ Top ORS
Elevation of Top ORS
(m)
1km
Gortdrum Mine
Displacement analysis along the Gortdrum Fault system
Offset in top ORS measured on cross sections with drill control
Datapoints every 100 – 200m in mine area
Lower data density in Gortdrum 3 & 4 faults
Notes: Top ORS isn’t present in FW but was projected (still good control)

## Slide 16
Copper in the Limerick Syncline?
Stacked Cu & Zn/Pb deposit
The question we all want answered (you know who you are)
  Is there another Gortdrum under Stonepark & Tobermallug?
* Radically alters the economics of both deposits *
Two main challenges (and possible solutions)
Fluid Chemistry
  Could the Zn+Pb be the exhaust of a Cu system? Or different system more likely?
Scale & Structure
  Gortdrum is extremely localised against a fault but Stonepark/Tobemallug (currently) has poorly defined structure
    Difficult Targeting
Notes: I’m not the first person proposing this idea and I won’t be the last!
The difference here is an evaluation of how we can move toward de-risking such a target…

## Slide 17
Fluid Chemistry + Reactive Flow Modelling
    Could the same fluids be responsible for a stacked mineral system? Geochemical modelling could help answer this
    Can sulphur rich fluids penetrate deep enough to provide adequate sulphur for an economic deposit?
    What would happen to a deep Cu deposit if a later Zn + Pb rich fluid passed through later? Redissolve Cu?
Copper in the Limerick Syncline?
De-Risking Exploration
Examples of fluid characterisation & mixing from Silvermines
Courtesy of Terranta
Notes: Better understand the system

## Slide 18
Evidence pre-Variscan copper in normal faults
Allihies area of the Beara Peninsula
Major lodes of the Mountain Mine.
Ore-bearing, east–west-striking quartz veins directly related to early extensional, basinal normal faults.
Molybdenite Re–Os dating of main-stage Cu lode: 367.3 ± 5.5 to 366.4 ± 1.9 Ma.
Lang et al. (2020) J. Geological Society 177(4)
wt% NaCleq
Th (deg C)
Notes: Uncertainty including all sources of analytical uncertainty plus decay constant.

## Slide 19
PL Boundaries
Copper in the Limerick Syncline?
Indicators of underlying structure
Stonepark & Pallas Green have a poorly defined structural model
How do we generate structural targets where structure is poorly defined?
Basic Base of reef model inputs
Base of Reef DH intersections
Base of reef sub-crop boundary
No faults included in model
Notes: Idea was to see any patterns that the BOR contours might suggest
All work done on both sytems has struggled to highlight any significant structures that are typical in Irish Deposits.

## Slide 20
Base of Reef Elevation
PL Boundaries
“Ski Slope”
Stonepark
Tobermallug
Stonepark & Pallas Green have a poorly defined structural model
How do we generate structural targets where structure is poorly defined?
Basic Base of reef model inputs
Base of Reef DH intersections
Base of reef sub-crop boundary
No faults included in model
Main Observations
Subtle right - stepping in base of reef
Large orebody sitting at intersection of ski slope and right stepping lineament
Copper in the Limerick Syncline?
Indicators of underlying structure
Notes: Dave Blaney will likely show a lot of NW oriented structures but will also probably say that larger structures haven’t been identified.
The main message to convey here is that there is likely some underlying larger structures that could be Cu targets in close proximity to faulting
General Observations
Base of reef has 2 main structural domain –
  the gently dipping/flattish area around Stonepark / Tobermalug
  The domain dipping steeply to the south (boundary between the 2 domains is the NW trending “ski-slope”)
On the northern margin of the map, are a series of apparent right stepping closely spaced contours, remeniscient of a right stepping normal fault system
Highest mineralisation sits close to where these two lineaments intersect.
There is undoubtedly also a NW – SE pattern to the mineralisation at Tobermallug too.
  I suggest the best mineralisation is where it is because of the intersection of these NW lineament with an underlying NE-SW structural grain creating fluid permeability pathways

## Slide 21
Blue book synthesis suggests ±350 m from Base of Reef to top ORS
Copper Targets starting from ~650 m drillhole length
  Glencore are already drilling +1400 m DHs
N
S
Base of reef
Top of Reef
Reef thinned by explosive volcanism (Pyroclastic Infill)
Faults expressed as subtle rollovers in Base of Waulsortian
300m
300m
0m
-300 m
-600 m
-900 m
-1200 m
Topography
Projected Top ORS
Cu
Cu
650 – 700 m Target
900 - 1000m
Target
Copper in the Limerick Syncline
What could a target look like?
Notes: These structures are very hypothetical, but I wanted to get them thinking about how a target could look…
Do the diatremes help pick out structural lineaments? Could they help us site a drillhole targeting a fault bounded Cu deposit?
I think the hinge point of the ski slope would be an ideal target… Even if the fault is antithetic to a larger fault downdip, it has big potential for fracture enhanced permeability.
They’re already drilling deeper than 1400 m down the ski slope so why not invest and test the bigger money prize?

## Slide 22
Conclusions
Blue book synthesis highlights main growth centres and lithological variation in the lower Carboniferous stratigraphy
Gortdrum was likely a segmented normal fault system
Copper Targets starting from
~650 m below surface in the
Limerick Syncline

## Slide 23
With support from:
This presentation has emanated from research supported in part by a research grant from Science Foundation Ireland (SFI) under Grant Number 16/RP/3849 & 13/RC/2092_P2.
The authors would like to thank the Geological Survey Ireland (GSI), Geoscience Regulation Office (GSRO) of the Department of the Environment, Climate and Communications (DECC), Ireland, for providing access to released well, seismic and potential field datasets.
All rights reserved on the content, images and data within this presentation.
Acknowledgments
Academic Software licences